## Slide 1: Design and Optimization of a Blended Wing Body UAV Using AI-Driven Surrogate Modeling and CFD Analysis
Dr. Muhammad Shoaib Naseem, M Uns Haider Shah, M Nasih Ul Hassan, Rimsha Zubair, Ayman Afzal
Presented By: Muhammad Uns Haider Shah

## Slide 2: Introduction & Research Goal
Introduction:
Blended Wing Body (BWB) UAVs offer high aerodynamic efficiency by integrating the wing and fuselage.
Limited propulsion power at small scales restricts endurance.
Research Goal:
Increase UAV endurance using a low‑power propulsion system through surface topology optimization using AI‑driven geometry optimization.

## Slide 3: Significance
Key Impact:
Extended gliding time without propulsion provides critical extra seconds in emergencies.
Enhances occupants’ safety by allowing longer unpowered flight for controlled emergency landings.
Potential to save lives and improve overall aerospace safety

## Slide 4: Motivation for Surrogates
Full-fidelity CFD: minutes-to-hours per run
Large design space: span, sweep, twist, taper, airfoils…
Goal: Millisecond evaluations to drive rapid optimization

## Slide 5: Workflow Overview
Sample 50 wing geometries data
Preprocess data (normalization, train/test split)
Train MLP surrogate
Predict performance
Optimize geometry via AI loop

## Slide 6: Dataset & Features
Inputs (m=10): span, root & tip chords, quarter-chord sweep, taper, twist, 3 airfoil IDs
Outputs: L/D, drag coefficient, required power
Latin-Hypercube sampling ensures space-filling

## Slide 8: Model Comparison
MLP (2×50 neurons) best: RMSE<0.02, R²>0.98
Nonlinear models outperform linear baseline

## Slide 9: MLP Architecture
Layers: Input → 50 neurons → 50 neurons → Output
Activation: ReLU
Solver: Adam

## Slide 10: Rapid Design Exploration
Time Comparison:
  CFD run: ~30 min
  Surrogate eval: <0.001 s
Enables 10⁴–10⁵ candidates in the same time

## Slide 11: Integration with Optimization
Genetic Algorithm or Bayesian Optimizer
Surrogate as objective function
Final top candidates validated by CFD

## Slide 12: Initial CAD Model

## Slide 13: Parameters for Final Design
Airfoil Selection:
Root/Center: Selig S1223
Mid: NACA 1408
Wing: NACA 0012
Wingspan:1.0 m
Root Chord: ~0.30 m
Tip Chord: ~0.15 m
Wing Sweep Angle (Λ): 20°–35°
Taper Ratio(λ): ~0.5
Aspect Ratio= 6–8
Wing Twist (θ): ±0°–±3°
Blending Region: Defined via spline/Bezier curves

## Slide 14: Winglet Parameters
Winglet Root : ~0.10–0.12 m
Winglet Tip : ~0.05–0.07 m
Winglet Sweep: 10°–20°
Winglet Cant Angle: 15°–30°
Winglet Twist: ±0°–±2°

## Slide 15: Final CAD Model

## Slide 16: CFD Simulation Setup
Solver & Physics
3D, steady pressure‐based RANS
SST k–ω turbulence with heat transfer enabled
Flow Conditions
Free-stream velocity:
1) 30 m/s (Mach 0.088)
2) 240 m/s (Mach 0.7)
Inlet far-field: T = 300 K, turbulence intensity = 5 %, viscosity ratio = 10
Boundary Conditions
Pressure-farfield inlet/outlet
No-slip, adiabatic aluminum walls
Symmetry on vertical side planes

## Slide 17: CFD Key Aerodynamic Results @ 30 m/s
Lift Coefficient (CL)= 0.44
Drag Coefficient (CD) = 0.004
Lift-to-Drag Ratio (L/D) ≈ 110

## Slide 18: CFD Key Aerodynamic Results @ 240 m/s
Lift Coefficient (CL)= 0.04
Drag Coefficient (CD) = 0.004
Lift-to-Drag Ratio (L/D) ≈ 10

## Slide 19: volume mesh

## Slide 20: wing mesh

## Slide 21: Pressure Lower

## Slide 22: Pressure Upper

## Slide 23: Velocity mach (mid)

## Slide 24: Velocity mach (root)

## Slide 25: Velocity mach (tip)

## Slide 26: Velocity Vector (mid)

## Slide 27: Velocity Vector (root)

## Slide 28: Velocity Vector (tip)

## Slide 29: Velocity X (mid)

## Slide 30: Velocity X (root)

## Slide 31: Velocity X (tip)

## Slide 32: Lift-to-Drag Ratio Comparison at 30 m/s (Mach 0.088)
High-performance gliders: L/D 30–60
Light single-engine aircraft (e.g., Cessna 172): L/D 9–12
Long-endurance UAVs: L/D 12–20
Commercial airliners L/D 12–16
Military jets: L/D 5–8

## Slide 33: Lift-to-Drag Ratio Comparison at 30 m/s (Mach 0.088)
For designed UAV: L/D is 110
Surpasses High-performance gliders, typical UAVs and light aircrafts.
Efficiency will be nearly matching high-performance gliders, enabling extended endurance or reduced power requirements in real world conditions.

## Slide 34: Lift-to-Drag Ratio Comparison at 240 m/s (Mach 0.7)
High-performance UAVs (jet-powered)
• L/D ≈ 8–15
• For Designed UAV = 10

## Slide 35: Q&A